## Slide 1: Network Layer: IP Addressesing GitHub - AhmadNawaz110/CE313-Computer-Commincation-and-Network-Spring-2026-
CE313
Computer Communication & Networks
Engr. M Ahmad Nawaz
Engr.ahmad.nawaz@giki.edu.pk
Notes: As we know, most of the applications like HTTP, FTP requires reliability. Furthermore, we know that TCP provides reliability Service. Before going in to the detail how TCP reliability mechanism works. Lets built a reliable data transfer protocol step by step in order to understand the underlying challenges, which are addressed by TCP.

## Slide 2: What is an IPV4 Address?

## Slide 3: Address Space
addr15
addr1
addr2
addr41
addr31
addr226
…………..
…………..
…………..
…………..
…………..
…………..
…………..

## Slide 4: Address space rule
…………..
…………..
The address space in a protocol That uses N-bits to define an Address is:
2N

## Slide 5: IPv4 address space
The address space of IPv4 is 232
or 4,294,967,296.
Notes: 232
or 4,294,967,296

## Slide 6
01110101 10010101 00011101 11101010
Binary Notation

## Slide 7: Dotted-decimal notation

## Slide 8: Example 3
Solution
Find the error in the following IP Address 111.56.045.78
There are no leading zeroes in Dotted-decimal notation (045)

## Slide 9: Example 3 (continued)
Solution
Find the error in the following IP Address 75.45.301.14
In decimal notation each number <= 255 301 is out of the range

## Slide 10: CLASSFUL ADDRESSING

## Slide 11: In classful addressing the address space is divided into 5 classes:
A, B, C, D, and E.

## Slide 12: Finding the class in binary notation

## Slide 13: Finding the address class

## Slide 14: Example 5
Show that Class A has
231 = 2,147,483,648 addresses:
In class A, only 1 bit defines the class. The remaining 31 bits are available for the address. With 31 bits, we can have 2^31 or 2,147,483,648 addresses.

## Slide 15
Example 6
Solution
Find the class of the following IP addresses
00000001 | 00001011 | 00001011 11101111
11000001 | 00001011 | 00001011 11101111
00000001 00001011 00001011 11101111
1st is 0, hence it is Class A
11000001 00001011 00001011 11101111
1st and 2nd bits are 1, and 3rd bit is 0 hence, Class C

## Slide 16: Finding the class in decimal notation

## Slide 17
Example 7
Solution
Find the class of the following addresses 158.223.1.108
227.13.14.88
158.223.1.108
1st byte = 158 (128<158<191) class B
  227.13.14.88
1st byte = 227 (224<227<239) class D

## Slide 18: IP address with appending port number
158.128.1.108:25
the four octet before colon is the IP address
The number after colon (25) is the port number

## Slide 19: Netid and hostid

## Slide 20: Blocks in class A

## Slide 21: Blocks in class B

## Slide 22: Blocks in class C

## Slide 26: Network Addresses
The network address is the first address.
The network address defines the network to the rest of the Internet.
Given the network address, we can find the class of the address, the block, and the range of the addresses in the block

## Slide 28
Example 8
Solution
Given the network address 132.21.0.0, find the class, the block, and the range of the addresses
The 1st byte is between 128 and 191.
Hence, Class B
The block has a netid of 132.21.
The addresses range from 132.21.0.0 to 132.21.255.255.

## Slide 29: Mask
A mask is a 32-bit binary number.
The mask is ANDeD with IP address to get
  The block address (Network address)
  Mask And IP address = Block Address

## Slide 30: Default Mask
Class A default mask is 255.0.0.0
Class B default mask is 255.255.0.0
Class C Default mask 255.255.255.0

## Slide 31: Subnet Mask
An IP address has 2 parts:
  The Network identification.
  The Host identification.
Frequently, the Network & Host portions of the address need to be separately extracted.
In most cases, if you know the address class, it’s easy to separate the 2 portions.

## Slide 32: Subnet Mask (Cont.)
With the rapid growth of the internet & the ever-increasing demand for new addresses, the standard address class structure has been expanded by borrowing bits from the Host portion to allow for more Networks.
Under this addressing scheme, called Subnetting, separating the Network & Host requires a special process called Subnet Masking.

## Slide 33: Subnet Mask (Cont.)
The subnet masking process was developed to identify & extract the Network part of the address.
A subnet mask, which contains a binary bit pattern of ones & zeros, is applied to an address to determine whether the address is on the local Network.
If it is not, the process of routing it to an outside network begins.

## Slide 34: Subnet Mask (Cont.)
The function of a subnet mask is to determine whether an IP address exists on the local network or whether it must be routed outside the local network.
It is applied to a message’s destination address to extract the network address.
If the extracted network address matches the local network ID, the destination is located on the local network.

## Slide 35: Subnet Mask (Cont.)
However, if they don’t match, the message must be routed outside the local network.
The process used to apply the subnet mask involves Boolean Algebra to filter out non- matching bits to identify the network address.

## Slide 36: A network with two levels of hierarchy (not subnetted)

## Slide 37: Note
Subnetting is done by borrowing bits from the host part and add them the network part

## Slide 38: Example 9
What is the subnetwork address if the destination address is 200.45.34.56 and the subnet mask is 255.255.240.0?

## Slide 39: Solution
AND OPERATION
11001000 00101101 00100010 00111000
11111111 11111111 11110000 00000000
11001000 00101101 00100000 00000000
The subnetwork address is 200.45.32.0.

## Slide 40: What is the subnetwork address if the destination address is 19.30.80.5 and the mask is 255.255.192.0?
Example 10
Solution
See next slide

## Slide 41: Solution

## Slide 42: Comparison of a default mask and a subnet mask

## Slide 44: A company is granted the site address
Example 11
201.70.64.0 (class C). The company needs six subnets. Design the subnets.
Solution
The number of 1s in the default mask is 24 (class C).

## Slide 45: Solution (Continued)
The company needs six subnets. This number 6 is not a power of 2. The next number that is a power of 2 is 8 (23). We need 3 more 1s in the subnet mask. The total number of 1s in the subnet mask is 27 (24  3).
The total number of 0s is 5 (32  27). The mask is

## Slide 46: Solution (Continued)
11111111 11111111 11111111 11100000
or
255.255.255.224
The number of subnets is 8.
The number of addresses in each subnet is 25 (5 is the number of 0s) or 32.

## Slide 47: Example 3

## Slide 48: A company is granted the site address
Example 12
181.56.0.0 (class B). The company needs 1000 subnets. Design the subnets.
Solution
The number of 1s in the default mask is 16 (class B).

## Slide 49: Solution (Continued)
The company needs 1000 subnets. The number is not a power of 2. The next number that is a power of 2 is 1024 (210). We need 10 more 1s in the subnet mask.
The total number of 1s in the subnet mask is 26 (16  10).
The total number of 0s is 6 (32  26).

## Slide 50: Solution (Continued)
The mask is
11111111 11111111 11111111 11000000
or
255.255.255.192.
The number of subnets is 1024.
The number of addresses in each subnet is 26 (6 is the number of 0s) or 64.

## Slide 51: Example 4

## Slide 52
Let us consider an example of Class B network 172.16.0.0. What will be the first and last IP address, if we want to create 2 subnets
Exercise

## Slide 53
Exercise
Let us consider an example of Class B network 172.16.0.0. What is will be the first and last IP address, if we want to create 6 subnets

## Slide 54: SUPERNETTING

## Slide 55: What is supernetting?
Supernetting is the opposite of subnetting
In subnetting you borrow bits from the host part
Supernetting is done by borrowing bits from the network side.
And combine a group of networks into one large supernetwork.

## Slide 56: A supernetwork

## Slide 57: Rules:
 The number of blocks must be a power of 2 (1, 2, 4, 8, 16, . . .).
 The blocks must be contiguous in the address space (no gaps between the blocks).
 The third byte of the first address in the superblock must be evenly divisible by the number of blocks. In other words, if the number of blocks is N, the third byte must be divisible by N.

## Slide 58: Which of the following set of class C blocks
Example 5
198.47.32.0 198.47.33.0 198.47.34.0
198.47.32.0 198.47.42.0 198.47.52.0 198.47.62.0
198.47.31.0 198.47.32.0 198.47.33.0 198.47.52.0
198.47.32.0 198.47.33.0 198.47.34.0 198.47.35.0
can be used to form a supernet for a company?

## Slide 59: Solution
1: No, there are only three blocks.
2: No, the blocks are not contiguous.
3: No, 31 in the first block is not divisible by 4. 4: Yes, all three requirements are fulfilled.

## Slide 61
In supernetting,
we need the first address of the supernet
and the supernet mask to define the range of addresses.

## Slide 62: Comparison of subnet, default, and supernet masks

## Slide 63: We need to make a supernetwork out of 16
class C blocks. What is the supernet mask?
Solution
We need 16 blocks. For 16 blocks we need to change four 1s to 0s in the default mask. So the mask is
11111111 11111111 11110000 00000000
or
255.255.240.0

## Slide 64: Example 14
A supernet has a first address of 205.16.32.0 and a supernet mask of 255.255.248.0. A router receives three packets with the following destination addresses:
205.16.37.44
205.16.42.56
205.17.33.76
Which packet belongs to the supernet?

## Slide 65: Solution
We apply the supernet mask to see if we can find the beginning address.
205.16.37.44 AND 255.255.248.0
205.16.42.56 AND 255.255.248.0
205.17.33.76 AND 255.255.248.0
 205.16.32.0
 205.16.40.0
 205.17.32.0
Only the first address belongs to this supernet.

## Slide 66: Example 15
A supernet has a first address of 205.16.32.0 and a supernet mask of 255.255.248.0. How many blocks are in this supernet and what is the range of addresses?
Solution
The supernet has 21 1s. The default mask has 24 1s. Since the difference is 3, there are 23 or 8 blocks in this supernet. The blocks are 205.16.32.0 to 205.16.39.0. The first address is 205.16.32.0. The last address is 205.16.39.255.