## Slide 1
CE313 COMPUTER COMMUNICATIONS & COMPUTER NETWORKS

## Slide 2: NETWORK SUPPORTING THE WAY WE LIVE

## Slide 3
What is Communication?

## Slide 4
What is Communication?
Communication is the process of exchanging information between two or more entities to convey meaning, intent, or data.

## Slide 5: What is Data Communication?
Data communications is the exchange of data between two devices via some form of transmission medium.
Data refers to information presented in whatever form that is agreed upon by the parties creating and using the data.

## Slide 6: Which of the following is NOT required for data communication?
A) Sender B) Receiver C) Transmission medium D) Internet connection

## Slide 7: Which of the following is NOT required for data communication?
A) Sender B) Receiver C) Transmission medium D) Internet connection ✅ (Reinforces that data comm works over ANY medium—not just internet)

## Slide 8: FUNDAMENTAL CHARACTERISTICS
Effectiveness of Data communications depends on following characteristics.
  Delivery
  Accuracy
  Timeliness
  Jitter

## Slide 9: Jitter
What it is | Fluctuation in the time between successive packet arrivals (e.g., packets should arrive every 20ms, but arrive at 15ms → 35ms → 22ms)
Why it matters | Critical for real-time applications: • Voice/video calls → choppy audio/video • Online gaming → lag spikes • Live streaming → buffering
Jitter vs. Delay | • Delay (latency) = Total time for a packet to travel • Jitter = Variation in that delay between packets
Causes | • Network congestion • Route changes • Queuing delays at routers/switches • Variable processing times
Mitigation | Jitter buffers: Temporarily store incoming packets to smooth out delivery timing before playback/processing

## Slide 10: Question
A live video call freezes for 2 seconds, then resumes with audio/video out of sync. Which TWO characteristics failed?

## Slide 11: Question
A live video call freezes for 2 seconds, then resumes with audio/video out of sync. Which TWO characteristics failed?
Answer: Timeliness + Jitter (tests distinction between delay vs. variation in delay

## Slide 12: COMPONENTS OF DATA COMMUNICATIONS
Message
Sender
Receiver
Transmission medium
Protocol

## Slide 13: PROTOCOLS
PROTOCOL
– A protocol is
a set of rules that govern data
a protocol
communications; the key Elements of are syntax, semantics and timing.
Syntax
  Structure or format of the data.
Semantics
  Meaning of each section of bits.
Timing
– When data should be sent, and how fast data can be sent.

## Slide 14: Question
If two devices use the same cable but different protocols, will communication succeed? Why?

## Slide 15: Question
If two devices use the same cable but different protocols, will communication succeed? Why?"
Key insight: Protocol mismatch = communication failure

## Slide 16: Question
In human conversation, "grammar rules" map to which protocol element? A) Syntax B) Semantics C) Timing

## Slide 17: Question
In human conversation, "grammar rules" map to which protocol element? A) Syntax ✅ B) Semantics C) Timing

## Slide 18: DATA REPRESENTATION
Information can be sent in different forms
  Text
  Numbers
  Images
  Audio
  Video

## Slide 19: DATA FLOW
Communication between two devices can be:
  Simplex
  Half-Duplex
  Full-Duplex

## Slide 20: DATA FLOW

## Slide 21: Question
Match the mode to the example:
Keyboard → Computer
Walkie-talkie
Phone call

## Slide 22: Question
Match the mode to the example:
Keyboard → Computer
Walkie-talkie
Phone call
Answers: 1=Simplex, 2=Half-Duplex, 3=Full-Duplex

## Slide 23: NETWORKS
A network is a set of devices (often referred to as nodes) connected by communication links. A node can be a computer, printer, or any other device capable of sending and/or receiving data generated by other nodes on the network.
An Interconnected system of things or people.

## Slide 24
Distributed Processing
  Most Networks uses distributed processing, in which task is divided among multiple computers.
Network Criteria
  A network must be able to meet certain number of criteria, the most important are:
    Performance
    Reliability
    Security

## Slide 25: TYPES OF PHYSICAL CONNECTION
Point-to-Point Connection
Multipoint Connection

## Slide 26: PHYSICAL TOPOLOGY
Way in which network is laid out physically. Two or more devices connect to a link; two or more links from a topology.

## Slide 27: MESH TOPOLOGY
Every device has a dedicated point to point link to every other device.
A fully connected mesh network has n(n-1)/2 physical channels to link n device.
Every device must have n-1 I/O ports.
Advantages:
  Eliminating traffic problems due to dedicated links.
  Robust.
  Privacy or security.
  Easy for fault identification and isolation.
Disadvantages:
  High cost due to amount of cabling and the network I/O ports required.
  Difficult and complex installment.

## Slide 28: FULLY CONNECTED MESH TOPOLOGY (FIVE DEVICES)

## Slide 29: Question
Calculation Sprint (15 sec): How many links in a fully connected mesh with 8 devices? A) 8 B) 28 C) 56 D) 64

## Slide 30: Question
Calculation Sprint (15 sec): How many links in a fully connected mesh with 8 devices? A) 8 B) 28 ✅ (8×7/2) C) 56 D) 64

## Slide 31: STAR TOPOLOGY
Each device has a dedicated point-to-point link only to a central controller, usually called hub.
Does not allow direct traffic between devices, the controller acts as an exchange.
Advantages:
  Less expensive then mesh topology.
  Easy to install and reconfigure.
  Robust
  Easy fault identification and fault isolation.
Disadvantages:
  Could be costly due to Hub but still highly recommended due to its advantages over other topologies.

## Slide 32: Star Topology with four stations

## Slide 33: Question
Fault Analysis: In a 20-device star network, one computer fails. What happens? A) Whole network fails B) Only that device is isolated C) Half the network fails D) Hub overheats

## Slide 34: Question
Fault Analysis: In a 20-device star network, one computer fails. What happens? A) Whole network fails B) Only that device is isolated ✅ C) Half the network fails D) Hub overheats → Reinforces robustness advantage

## Slide 35: BUS TOPOLOGY
One long cable acts as a backbone (Bus) to link all other devices (nodes) in a network. Nodes are connected to the bus cable by drop lines and taps.
Mesh, Star are point to point. Bus is multipoint.
Propagating signal through the bus starts fading due to loss of energy as heat. Thus there is a limit on the number of taps and the distance between those taps.
Advantages:
  Ease of installation.
Disadvantages:
  Difficult reconnection.
  Difficult fault isolation.
  A fault or break in the bus cable stops all transmission to the further segment.

## Slide 36: Bus Topology Connecting three stations.

## Slide 37: Question
Why does a break in the bus cable disable devices AFTER the break but not before it?

## Slide 38: Question
Why does a break in the bus cable disable devices AFTER the break but not before it?
Answer: Signal propagates linearly from sender; break blocks further propagation (tests understanding of signal flow)

## Slide 39: RING TOPOLOGY
Each device has a dedicated point-to-point connection only with the two devices on either side of it. A signal is passed along the ring in one direction, from device to device, until it reaches its destination.
Each device in the ring incorporates a repeater.
Advantages:
  Easy to install and reconfigure with considerations like maximum ring length and number of devices.
  Simplified fault isolation.
Disadvantage:
  Due to unidirectional traffic, a break in the ring can disable the entire network.

## Slide 40: Ring Topology connecting six stations.

## Slide 41: Question
True/False Rapid Fire: In ring topology, a repeater in each device amplifies signals to prevent degradation

## Slide 42: Question
True/False Rapid Fire: "In ring topology, a repeater in each device amplifies signals to prevent degradation." ✅ TRUE (Reinforces why rings can span longer distances than bus)

## Slide 43: HYBRID TOPOLGY

## Slide 44: CATEGORIES OF NETWORK
Network
Metropolitan area network (MAN)
Wide area network (WAN)
Local area network (LAN)

## Slide 45: LOCAL AREA NETWORK
Usually privately owned and links the devices in a single office, building or campus.
Geographical size is few kilometers.
Designed to allow resources (hardware, software or data) to be shared between personal computers or work stations.
In general use one type of media.
Topologies: bus, ring and star.
Data rates: 4 to 16 Mbps. Recent advancements support up to 100 Mbps and Gbps is in development.

## Slide 46: Question
Which topology is LEAST common in modern LANs? A) Star B) Bus C) Mesh D) Ring

## Slide 47: Question
Which topology is LEAST common in modern LANs?
A) Star ✅ (Most common today) B) Bus ❌ (Legacy Ethernet) C) Mesh ❌ (Rare due to cost) D) Ring ❌ (Token Ring obsolete)

## Slide 48: LAN connecting 12 computers in a Hub

## Slide 49: METROPOLITAN AREA NETWORK
Designed for the customers who need a high speed connectivity, normally to the internet and spread over a city or part of city.
Maybe a single network or maybe a means of connecting number of LANs into a larger network so that resources may be shared LAN-to-LAN as well as device-to-device.
Example: A company can use a MAN to connect LANs in all its offices throughout a city.

## Slide 50: Metropolitan Area Network

## Slide 51: Question
A university has campuses across a city. Each campus has its own LAN. What network type connects them for shared library resources?

## Slide 52: Question
A university has campuses across a city. Each campus has its own LAN. What network type connects them for shared library resources?"
→ Answer: MAN

## Slide 53: WIDE AREA NETWORK
Provides long distance transmission of data, voice, image and video information over large geographic areas that may comprise a country, a continent, or even the whole world.
Switched WAN:
  connects the end systems, which usually comprise a router (internetworking connecting device) that connects to another LAN or WAN
  complex as the backbones that connect the Internet.
Point-to-Point WAN:
  A line leased from a telephone or cable TV provider that connects a home computer or a small LAN to an Internet service provider (lSP).
  simple as a dial-up line that connects a home computer to the Internet

## Slide 54: A Switched WAN & Point-to-Point WAN

## Slide 55: A Heterogeneous Network made of 4 WANs and 2 LANs

## Slide 56: INTERNET

## Slide 57: Hierarchical Organization of Internet

## Slide 58: Question
Which WAN type uses routers to dynamically route traffic between multiple paths?

## Slide 59: Question
Which WAN type uses routers to dynamically route traffic between multiple paths?
→ Answer: Switched WAN (distinguishes infrastructure complexity

## Slide 60: STANDARDS
Standard products
are necessary to ensure that from different manufacturers can
work together as expected.
Data Communication Standards fall in to two categories.
  De facto
  De jure

## Slide 61: STANDARD ORGANIZATIONS
International Organization for Standardization (ISO)
International Telecommunication Union- Telecommunication Standards Sector (ITU-T)
American National Standards Institute (ANSI)
Institute of Electrical and Electronics Engineers (IEEE)
Electronics Industries Association (EIA)

## Slide 67: To-Do List
At least go through all the slides once in order to grasp the concept before the next lecture.
Join the Group Home page as soon as possible.
Lecture Slides for the next lecture will be uploaded on the group home page before the lecture.
Any concern regarding the course, email on the engr.ahmad.Nawaz@giki.edu.pk