## Slide 1
CE313 COMPUTER COMMUNICATIONS & COMPUTER NETWORKS

## Slide 2: HYBRID TOPOLGY

## Slide 3: CATEGORIES OF NETWORK
Network
Metropolitan area network (MAN)
Wide area network (WAN)
Local area network (LAN)

## Slide 4: LOCAL AREA NETWORK
Usually privately owned and links the devices in a single office, building or campus.
Geographical size is few kilometers.
Designed to allow resources (hardware, software or data) to be shared between personal computers or work stations.
In general use one type of media.
Topologies: bus, ring and star.
Data rates: 4 to 16 Mbps. Recent advancements support up to 100 Mbps and Gbps is in development.

## Slide 5: Question
Which topology is LEAST common in modern LANs? A) Star B) Bus C) Mesh D) Ring

## Slide 6: Question
Which topology is LEAST common in modern LANs?
A) Star ✅ (Most common today) B) Bus ❌ (Legacy Ethernet) C) Mesh ❌ (Rare due to cost) D) Ring ❌ (Token Ring obsolete)

## Slide 7: LAN connecting 12 computers in a Hub

## Slide 8: METROPOLITAN AREA NETWORK
Designed for the customers who need a high speed connectivity, normally to the internet and spread over a city or part of city.
Maybe a single network or maybe a means of connecting number of LANs into a larger network so that resources may be shared LAN-to-LAN as well as device-to-device.
Example: A company can use a MAN to connect LANs in all its offices throughout a city.

## Slide 9: Metropolitan Area Network

## Slide 10: Question
A university has campuses across a city. Each campus has its own LAN. What network type connects them for shared library resources?

## Slide 11: Question
A university has campuses across a city. Each campus has its own LAN. What network type connects them for shared library resources?"
→ Answer: MAN

## Slide 12: WIDE AREA NETWORK
Provides long distance transmission of data, voice, image and video information over large geographic areas that may comprise a country, a continent, or even the whole world.
Switched WAN:
  connects the end systems, which usually comprise a router (internetworking connecting device) that connects to another LAN or WAN
  complex as the backbones that connect the Internet.
Point-to-Point WAN:
  A line leased from a telephone or cable TV provider that connects a home computer or a small LAN to an Internet service provider (lSP).
  simple as a dial-up line that connects a home computer to the Internet

## Slide 13: A Switched WAN & Point-to-Point WAN

## Slide 14: A Heterogeneous Network made of 4 WANs and 2 LANs

## Slide 15: INTERNET

## Slide 16: Hierarchical Organization of Internet

## Slide 17: Question
Which WAN type uses routers to dynamically route traffic between multiple paths?

## Slide 18: Question
Which WAN type uses routers to dynamically route traffic between multiple paths?
→ Answer: Switched WAN (distinguishes infrastructure complexity

## Slide 20: STANDARDS
Standard products
are necessary to ensure that from different manufacturers can
work together as expected.
Data Communication Standards fall in to two categories.
  De facto
  De jure

## Slide 21: STANDARD ORGANIZATIONS
International Organization for Standardization (ISO)
International Telecommunication Union- Telecommunication Standards Sector (ITU-T)
American National Standards Institute (ANSI)
Institute of Electrical and Electronics Engineers (IEEE)
Electronics Industries Association (EIA)

## Slide 22: Layered Tasks
An example from the everyday life
Hierarchy?
Services

## Slide 23: Why layered communication?
To reduce complexity of communication task by splitting it into several layered small tasks
Functionality of the layers can be changed as long as the service provided to the layer above stays unchanged
  makes easier maintenance & updating
Each layer has its own task
Each layer has its own protocol

## Slide 24: Reference Models
OSI reference model
TCP/IP

## Slide 25: OSI Reference model
Open System Interconnection
7 layers
Crate a layer when different abstraction is needed
Each layer performs a well define function
Functions of the layers chosen taking internationally standardized protocols
Number of layers – large enough to avoid complexity

## Slide 26: Seven layers of the OSI model

## Slide 27: Exchange using OSI Model

## Slide 28: The interaction between layers in the OSI model

## Slide 29: Issues, to be resolved by the layers
Larger bandwidth at lower cost
Error correction
Flow control
Addressing
Multiplexing
Naming
Congestion control
Mobility
Routing
Fragmentation
Security
....

## Slide 30: OSI Layers

## Slide 31: Physical layer
Transporting bits from one end node to the next
type of the transmission media (twisted-pair, coax, optical fiber, air)
bit representation (voltage levels of logical values)
data rate (speed)
synchronization of bits (time synchronization)
physical
connection

## Slide 32
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.
Note

## Slide 33: Data Link layer
Transporting frames from one end node to the next one
logical
connection
- framing - physical addressing
- flow control - error control
access control

## Slide 34: Data Link layer - hop-to-hop delivery-

## Slide 35: Data Link layer - example-

## Slide 36
The data link layer is responsible for moving frames from one hop (node) to the next.
Note

## Slide 37: Readings
Chapter 1 (B. A Forouzan)
  Section 1.1, 1.2, 1.3,1.4
Chapter 2 (B.A Forouzan)
  Section 2.1, 2.2

## Slide 44: To-Do List
At least go through all the slides once in order to grasp the concept before the next lecture.
Join the Group Home page as soon as possible.
Lecture Slides for the next lecture will be uploaded on the group home page before the lecture.
Any concern regarding the course, email on the engr.ahmad.Nawaz@giki.edu.pk