## Slide 1: Computer Communication & Networks
Week 4
Datalink Layer: Datalink control and protocols
GitHub - AhmadNawaz110/CE313-Computer-Commincation-and-Network-Spring-2026-
Engr. M Ahmad Nawaz
Engr.ahmad.nawaz@giki.edu.pk

## Slide 2: IEEE STANDARDS
In 1985, the Computer Society of the IEEE started a project, called Project 802, to set standards to enable intercommunication among equipment from a variety of manufacturers. Project 802 is a way of specifying functions of the physical layer and the data link layer of major LAN protocols.

## Slide 3: IEEE standard for LANs

## Slide 4: HDLC frame compared with LLC and MAC frames

## Slide 5: STANDARD ETHERNET
The original Ethernet was created in 1976 at Xerox’s Palo Alto Research Center (PARC). Since then, it has gone through four generations. We briefly discuss the Standard (or traditional) Ethernet in this section.
Topics discussed in this section:
MAC Sublayer Physical Layer

## Slide 6: Ethernet evolution through four generations

## Slide 7: 802.3 MAC frame

## Slide 8: Minimum and maximum lengths

## Slide 9
Frame length: Minimum: 64 bytes (512 bits)
Maximum: 1518 bytes (12,144 bits)
Note

## Slide 10: Ethernet address in hexadecimal notation

## Slide 11: Unicast and multicast addresses

## Slide 12
The least significant bit of the first byte defines the type of address.
If the bit is 0, the address is unicast; otherwise, it is multicast.
Note

## Slide 13: Note
The broadcast destination address is a special case of the multicast address in which all bits are 1s.

## Slide 14: Example Define the type of the following destination addresses:
a. | 4A:30:10:21:10:1A | b. | 47:20:1B:2E:08:EE
c. | FF:FF:FF:FF:FF:FF |  | 
Solution
To find the type of the address, we need to look at the second hexadecimal digit from the left. If it is even, the address is unicast. If it is odd, the address is multicast. If all digits are F’s, the address is broadcast. Therefore, we have the following:
This is a unicast address because A in binary is 1010.
This is a multicast address because 7 in binary is 0111.
This is a broadcast address because all digits are F’s.

## Slide 15: Categories of Standard Ethernet

## Slide 16: Encoding in a Standard Ethernet implementation

## Slide 17: 10Base5 implementation

## Slide 18: 10Base2 implementation

## Slide 19: 10Base-T implementation

## Slide 20: Summary of Standard Ethernet implementations

## Slide 21: CHANGES IN THE STANDARD
Bridged Ethernet Switched Ethernet Full-Duplex Ethernet
The 10-Mbps Standard Ethernet has gone through several changes before moving to the higher data rates. These changes actually opened the road to
the evolution of the Ethernet to become
compatible with other high-data-rate LANs.
Topics discussed in this section:

## Slide 22: Sharing bandwidth

## Slide 23: A network with and without a bridge

## Slide 24: Collision domains in an unbridged network and a bridged network

## Slide 25: Switched Ethernet

## Slide 26: Full-duplex switched Ethernet

## Slide 27: FAST ETHERNET
Fast Ethernet was designed to compete with LAN protocols such as FDDI or Fiber Channel. IEEE created Fast Ethernet under the name 802.3u. Fast Ethernet is backward-compatible with Standard Ethernet, but it can transmit data 10 times faster at a rate of 100 Mbps.

## Slide 28: Fast Ethernet topology

## Slide 29: Fast Ethernet implementations

## Slide 30: Summary of Fast Ethernet implementations

## Slide 31: GIGABIT ETHERNET
The need for an even higher data rate resulted in the design of the Gigabit Ethernet protocol (1000 Mbps). The IEEE committee calls the standard 802.3z.

## Slide 32: In the full-duplex mode of Gigabit Ethernet, there is no collision; the maximum length of the cable is determined by the signal attenuation in the cable.
Note

## Slide 33: Topologies of Gigabit Ethernet

## Slide 34: Gigabit Ethernet implementations

## Slide 35: Summary of Gigabit Ethernet implementations

## Slide 36: Summary of Ten-Gigabit Ethernet implementations

## Slide 37: THANK YOU FOR YOUR ATTENTION